## Slide 1: High Power Double-Clad Fiber Laser
Matt Ruby & Colin Diehl

## Slide 2
Single-mode Fiber
High Beam Quality
Low Propagation Loss
Lower Power Pump
Expensive
Multimode Fiber
Higher Power Pump
Inexpensive
Poor Beam Quality
High Propagation Loss

## Slide 3: Double-Clad Fiber
Laser light propagates in single-mode core
Pump light propagates in inner cladding

## Slide 4: Laser Construction

## Slide 5: Erbium-Ytterbium Co-Doped Fiber
Erbium-Ytterbium co-doped gain medium
980 nm pump laser
Radiationless decay
Stimulated emission of 1550 nm

## Slide 6: Box Layout

## Slide 7: Box Layout

## Slide 8: Box Layout

## Slide 9: Laser Construction

## Slide 10: Output Power
1.5 m EYDF 90/10 Coupler

## Slide 11: New Laser Construction

## Slide 12: Output Power
3 m EYDF 90/10 Coupler

## Slide 13: Laser Spectrum

## Slide 14: Laser Self Pulsing
Pulsing condition
  Low pump power
    When the pump is not able to maintain a complete population inversion, then the gain medium acts like a saturable absorber.
  Long cavity length
    When the cavity length is long the light pulse will have more time till it is fed back into the gain medium, allowing the pump time to start saturating the gain medium again.

## Slide 15: Evidence of Self Pulsing
Our laser has the right specs for self pulsing
  Long erbium fiber ~ (3m)
  Very long cavity ~ (12.5m)
Output @ 1540nm and 975nm /w 500mW pump

## Slide 16: Conclusion
Self pulsing verified
  By correlating the pump and signal oscillations at different pump powers.
  Pulsing is suppressed after about 550mW pump
  Pulse frequency increases with pump power
Conclusion
  We have shown that self pulsing in our fiber laser is a problem at pump powers lower than 500mW, though this is not a problem as our setup can supply more than enough power to suppress the pulsing.

## Slide 17: Future Work
Add frequency selective components
  Braggs grating
  Fabry-Perot Cavity
Fine frequency measurement
  Fabry-Perot Cavity
Higher power pump laser